## Slide 1: Streamline Drawing Creation with Newer SOLIDWORKS Drawing Tools
By Matthew Lorono
Product Definition Manager
SOLIDWORKS

## Slide 2: Matthew Lorono: Who am I?
Product Definition Manager for Drawings and MBD
Product Definition team looks at many sources to determine enhancements for each major (yearly) release.
We actively interface with customers on SOLIDWORKS Forums.
We process Enhancement Requests submitted by our customers.
We meet with customers face-to-face at events like SOLIDWORKS WORLD.
We conduct over 100 customer visits each year, learning on-site directly from customers about how SOLIDWORKS is and is not meeting your product needs.
  We also offer a program where we can work within a customer’s operation for 3 to 5 days as “one of the minions” to learn first-hand about what you are experiencing in your daily use of our applications.
We use everything we learn from interacting with customers to design changes for each major release of SOLIDWORKS and other products.
We valid our designs with Alpha and Beta testing.

## Slide 3: Zoom to Sheet
2015
Open 500-0008.slddrw from “Missed\500-SWW17” folder.
Press “F” key. Note the result zooms to include everything.
Click on “Zoom to Sheet”. The drawing zooms to the sheet regardless to elements beyond the sheet.

## Slide 4: On-the-fly sheet scale
2016
With 500-0008.slddrw still open, find the scale in the Status Bar.
Click on the scale to pop up the sheet scale menu.
Select 1:1.
Click on status bar scale to open the sheet scale menu again.
Note that Sheet Properties dialog is also available from the same menu.

## Slide 5: Drawing Zones and Automatic Borders
2015 and 2016
Goto the Sheet Format tab.
Click Edit Sheet Format.
Click Automatic border.
By-pass first page with Next button.

## Slide 6: Drawing Zones and Automatic Borders
2015 and 2016
Change Zone rows and columns to 4 and 4.
Change Region to Margins.
Change Left Margin to be 1in.
Note how changes affect on-screen display of the drawing’s border.
Click OK.

## Slide 7: Drawing Zones
2015
Click on Sheet Scale from the Status Bar.
Choose Sheet Properties.
Choose Zone Parameters.
Change Zone back to 2 rows and 2 columns, then click Apply Changes.

## Slide 8: Location Labels
2015
Switch to Annotation tab on CommandManager.
In the Commands entry field, type “Location label”.
When Location Label appears, drag it to the CommandManager under Revision Cloud.
Click on Location Label.
Click on Detail C view.
Sheet
Zone

## Slide 9: Zones in Revision Table
2015
Zoom to Revision Table and click the B hover icon on the lower left corner.
Place Revision symbols throughout the drawing.

## Slide 10: Add Zones to Annotations and Table
2015
Double click on Revision B description cell.
Change Feature Tree tab to PropertyManager.
Click Add Zone button.
Select Drawing View1.

## Slide 11: Assigning Center Marks to Layers
2013
Right click on open area of the drawing.
Select Change Layer.
Change current layer to Per Standard.
Click on Center Mark from Annotations tab of the CommandManager.
Change center mark to Linear Center Mark.
Add center marks to the top two holes only.

## Slide 12: Add Center mark to a set of center marks
2015
Right-click on current center mark.
Choose Add to Center Mark Set.
Click on the remaining two holes in the view.

## Slide 13: Add center marks to slots
2014
Start Center Mark command again.
Click on either arc of the top middle slot.

## Slide 14: Center Mark scaling
2016
Goto Tools>Options…>Document Properties>Centerline/Center Marks.
Uncheck Scale by view scale. This will set the center mark scale to the sheet instead of the view.
Turn this setting off

## Slide 15: All Caps
2014
Click to select the general notes in the lower left.
In the PropertyManager, add check to All uppercase.

## Slide 16: Expanded Paragraph Properties
2015
Double-click on the those notes to edit them.
Highlight the numbered paragraphs.
In the pop-up shortcut menu, select Paragraph Properties.
Increase spacing between paragraphs; then change number order to be from the bottom. Then OK.

## Slide 17: Revision Clouds
2013
From the Annotations tab on the CommandManager, click on Revision Cloud.
Click on Detail C to create a revision cloud.
Experiment with other settings.

## Slide 18: Drawings watermark
2013
From the Sheet Format tab of CommandManager, choose Edit Sheet Format.
Create a note. While editing, click on the Link Property icon in the PropertyManager.
Choose property named “Release Status”.
Highlight the note and change font size to 72. Also, rotate the note 20degs.
Exit edit mode and select the note.
Using Line Color tool of the Line Format toolbar, change the note color to a light gray.
In the PropertyManager, add check to Behind sheet.
Exit back to Drawing Sheet.

## Slide 19: Attach annotation to view or sheet
2014
Right-click on the general notes.
Select Attachment>Attach to Sheet.
Remember this issue?

## Slide 20: Section View Assist
2013
Delete existing cutting line.
Start Section View command (select from View Layout tab of the CommandManager).
Click on the inside diameter of the middle hole.
Click on Single Offset from the pop up toolbar.
Place the blue dot as shown in this bottom image.
Click on the upper right hole to finish the offset.
Click on OK, then place the new section view.

## Slide 21: Convert View to Sketch
2013
Right-click on the isometric view.
Select Convert View To Sketch.
Select Replace view with sketch in the PropertyManager, and click OK.

## Slide 22: On-the-fly dimensioning to Virtual Sharp
2014
From Annotation tab on the CommandManager, click on Smart Dimension.
On Drawing View, right-click on this edge.
Click on Find Intersection.
Click on opposite edge.
Repeat for the other side.
Place dimension.

## Slide 23: Replace Model for Drawing Views
2014
SM-1100.SLDPRT replaced with SM-1100.SLDASM
Save 500-0008.SLDDRW.
Open SM-1100.SLDDRW.
Goto Tools pullddown and click on Replace Model.
Add check to All Views.
Click on Browse and select “SM-1100.SLDASM”
Click OK.
Close drawing.

## Slide 24: Automatically splitting tables horizontally at a row
2014
Open 500-0000.SLDDRW.
Right-click on BOM.
Click on Horizontal Auto Split.
Set Max rows to 5.
Select Continuously.
Click on Apply.
Close drawing.

## Slide 25: Angular Running Dimensions
2014
Open flowbody-01.SLDDRW.
From these Dimensions toolbar, click Angular Running Dimension.
Click on model edge of the large diameter around middle bore.
Click on the top most mounting whole.
Click on each of the remaining mounting holes in any order.
Click on 0deg to drag the dimension set outward.
Experiment with PropertyManager settings under Leaders tab.
Close drawing.

## Slide 26: Angle Dimension from imaginary line
2015
Open Forming Tool-01.SLDDRW.
Start Smart Dimension command.
Click on the tip vertex.
Click on the right arrow with the cross appears.
Click on the right slope.
Place dimension.

## Slide 27: Flip an angle dimension to its vertically opposite
2015
Start Smart Dimension command.
Click on the right slope.
Click on the left slope.
Hold down ALT.
Place dimension where shown.

## Slide 28: Flip an angle dimension to its explementary angle
2015
Start Smart Dimension command.
Click on the right slope.
Click on the left slope.
Place 90deg dimension here.
Right-click on 90deg dimension.
Click on Explementary Angle.

## Slide 29: Spline Leader
2015
From the Annotation tab on the CommandManager, click on Balloon.
Place balloon with leader.
Exit Balloon command.
Select the balloon.
In the PropertyManager, select More Properties… button.
Click on Spline Leader button.
Click OK.
Drag spline controls as desired.
Close drawing.

## Slide 30: Foreshortened Linear Dimensions
2016
Open 500-0008.slddrw again.
Start Smart Dimension.
Click on the left model edge in Detail C.
Click on the opposite model edge in the parent view Drawing View5.
Place dimension.

## Slide 31: Apply Flag Notes
2016
Edit the general notes in the lower left of the drawing.
Click on #4.
In the PropertyManager, change balloon type to Triangle, then add check to Add to Flat Note Bank.
Click OK.
Start Balloon command.
Add check to Flag Note Bank in the PropertyManager.
In Drawing View5, click on the construction line point the balloon.
Then, place the balloon as shown here.
Close this drawing.

## Slide 32: Model Break Views in Drawings
2016
Break cuts at an angle are now available.
Actual break cut geometry carries over from the model.
Open HexEndPipe-01.SLDDRW.
Click on either view and select Open Part.
Goto Insert pulldown>Model Break View.
Select Orientation field, then select this face.
Drag green and red plans farther apart.
Goto Styles tab and select Pipe.
Click OK.
Return to the drawing.
Click on either view.
Add check to Show in exploded or model break state, then OK.

## Slide 33: Rearranging and sorting Balloon Stacks
2015
Open 500-0000.slddrw.
Zoom in on this stacked balloon.
Hold down SHIFT key and click on the 2 to drag it to the end. (Release SHIFT when done)
Right-click on the stack.
Click on Sort Stack.

## Slide 34: Link to Any Property
2016
Edit general notes to create a new note #1 that states “1. MATERIAL 500-0008 IS Magnesium Alloy”. Instead of typing the material, click on the Link to Property button in the PropertyManager.
Change first setting to “Model found here”.
Change drop down to “Selected component or other drawing view”
Select 500-0008 (item 9) from any view on the drawing.
In the Property name field, select “Material”
Exit the edit mode.

## Slide 35: Link to Any BOM Cell
2016
Edit general notes again. In note #1, erase “500-0008”.
In its place, type “Item #”
After the “#”, click on Link Table Cell button. This enters you in the table cell selection mode.
Pan to the BOM.
Click on the cell in the Item No. column with “9”.
Click on Link Table Cell button again to exist selection mode.
Click OK.
Close Drawing.