## Slide 1: Model-Based Definition using SOLIDWORKS MBD
By Matthew Lorono
Product Definition Manager
SOLIDWORKS

## Slide 2: Matthew Lorono: Who am I?
Product Definition Manager for Drawings and MBD
Product Definition team looks at many sources to determine enhancements for each major (yearly) release.
We actively interface with customers on SOLIDWORKS Forums.
We process Enhancement Requests submitted by our customers.
We meet with customers face-to-face at events like SOLIDWORKS WORLD.
We conduct over 300 customer visits each year, learning on-site directly from customers about how SOLIDWORKS is and is not meeting your product needs.
  We also offer a program where we can work within a customer’s operation for 3 to 5 days as “one of the minions” to learn first-hand about what you are experiencing in your daily use of our applications.
We use everything we learn from interacting with customers to design changes for each major release of SOLIDWORKS and other products.
We valid our designs with Alpha and Beta testing.

## Slide 3: Model Based Definition (MBD)
What is it?
MBD is the practice of using Product and Manufacturing Information (PMI) and other details within 3D CAD software as specifications for individual components and product assemblies…
…instead of creating and using drawings.

## Slide 4: Model Base Definition Types of Standards

## Slide 5: Standards for Model Based Definition
ASME and ISO
ASME Y14.41-2012 codifies MBD requirements for both 3D CAD software and CAD users. It covers:
Annotation placement and behaviors
How to use MBD in conjunction with electronic drawings
How to use MBD without drawings.

## Slide 6: Standards for Model Based Definition
ASME and ISO
ISO 16792:2006 was released by ISO.
It is a near copy of ASME Y14.41-2003.

## Slide 7: Standards for Model Based Definition
ASME and ISO
MIL-STD-31000 Rev A released in 2013 establishes requirements for Technical Data Packages (TDP) using MBD.

## Slide 8: Core Model Base Definition Strategies
No model annotations or dimensions
Basic model, general tolerance and “critical” dimensions
Full PMI within the 3D Model document

## Slide 9: Methods of Model Based Definition
No annotations or dimensions added to the model
The product definition is taken directly from interaction with the model by using measurement tools and feature dimensions (if available).
¤¡

## Slide 10: Methods of Model Based Definition
No annotations or dimensions added to the model
Best used for:
  One-off products with no supply-chain downstream documentation requirements (such as personal hobby projects).
  Prototyping phases during a project
  In conjunction with Fully Defined Drawings where the drawing is the final authority for product definition.
¡¤

## Slide 11: Methods of Model Based Definition
Basic model, general tolerance with “critical” dimensions
A common method is available to provide general tolerance using ASME Y14.5-2009. When employed, a note should state that the entire 3D model is BASIC.
  Profile feature control frame with datum scheme, and a note stating that the profile applies to all undefined features. Datums are either added in the 3D Model or on a separate Limited Dimension Drawing. This applies ALL OVER when included within a general note.
¤

## Slide 12: Methods of Model Based Definition
Full PMI within the 3D model document
All elements of PMI directly defining the product are carried within the 3D model document. All features are fully defined with directly applied dimensions and tolerances.
¤¡

## Slide 13: Methods of Model Based Definition
Full PMI within the 3D model document
This method is best used for:
  Completely drawing-free engineering and manufacturing environments
  New government and military contracts
¡¤

## Slide 14: SOLIDWORKS Settings to Optimize Model Base Definition
System Options
Part and Assembly Templates

## Slide 15: Preparing SOLIDWORKS for MBD
System Options for Parts and Assemblies
On the Display/Selection page:
  £ Display dimensions flat to screen (uncheck)
  Display notes flat to screen (uncheck)
These settings turned off will make it easy to format the PMI in the modelling environment.

## Slide 16: Preparing SOLIDWORKS for MBD
Document Properties for Part and Assembly Templates
On the Detailing page:
  Always display text as the same size (uncheck)
  Set the Text scale at the appropriate level for best viewing results for the intended size range of the product
1:1
2:1

## Slide 17: Preparing SOLIDWORKS for MBD
Part and Assembly Templates
Just as the scale of drawing views are adjusted based on sheet size to meet certain viewing requirements, scale of annotations should be adjusted in the modelling environment based on the size of the product.
Have several parts and assemblies templates for various product size ranges that are common in your organization.

## Slide 18: Preparing SOLIDWORKS for MBD
View settings Part and Assembly Templates
View settings can also be controlled via the right-click menu on Annotations folder in Feature Tree.
All Annotations in View pulldown menu controls all annotations at once.

## Slide 19: Preparing SOLIDWORKS for MBD
View settings Assembly Templates
As of SOLIDWORKS 2015 in Assemblies, you can show assembly level annotations separately from component level annotations from the View pulldown menu.

## Slide 20: Annotation Views
What are Annotation Views?
Using Annotation Views
Reassigning Annotation Views

## Slide 21: What are Annotation Views?
And, why are they important for MBD?
Annotation Views are a collection of invisible parallel planes upon which dimensions, notes and other annotations are placed within the 3D model.
Annotations Views are best viewed as is normal to screen, based on model orientation.
Note: Even when “flat to screen” display options are set, annotations are still placed on invisible planes aligned to Annotation Views for placement of leaders, dimension lines, and establish a location within the model space.

## Slide 22: Using Annotation Views
Commands and messages
Upon creation, annotations are automatically added to the most likely Annotation View on a plane that is applicable to the associated geometry.
When no Annotation View is likely, SOLIDWORKS will ask to create a new one.
If an annotation is not placed on any Annotation View (usually by user choice), then that annotation will be placed in the Unassigned Items Annotation View.
Unassigned Items is the only Annotation View where annotations are not required to be on parallel planes to each other.

## Slide 23: Using Annotation Views
Commands and messages
Switch to an Annotation View: Right-click on the view in the Feature Tree and selected “Activate and Reorient”.
  Only dimensions that are visible in the selected Annotation View will be visible while normal to the screen.

## Slide 24: Using Annotation Views
Show and Hide
Annotation Views can be turned on and off, similar to layers on drawings.
  In the Feature Tree, right-click on view and select “Show” or “Hide” to change the visibility setting.

## Slide 25: Reassigning Annotation Views
Changing the Annotation View of a selected annotation
Right-click on the annotation.
Mouse over Change Annotation View (*xxxx). A list of valid Annotation Views will show up in the list.
Select another Annotation View to reassign the annotation.
SW2014 and previous releases:
SW2015:

## Slide 26: Notes Area Annotation View
Always flat to screen and relative to model.
In SOLIDWORKS 2014, a new type of annotation was introduced, called Notes Area. This is in compliance with ASME Y14.41 requirements.

## Slide 27: Using the right SOLIDWORKS Tools for Model Base Definition
DimXpert
Reference Dimensions
Combination of both

## Slide 28: Using SOLIDWORKS for Model Based Definition
Know which tools to use and when
DimXpert allows for quick creation of dimensions for a whole model in compliance with common methods for ASME Y14.5M-1994.
  DimXpert schemes can be applied to TolAnalyst to analyze tolerance stack-up of the model.
  DimXpert also has many display controls available in Document Properties.
Limitations:
    Cannot violate ASME Y14.5M-1994

## Slide 29: Using SOLIDWORKS for Model Based Definition
Know which tools to use and when
Reference Dimensions provide manual methods to create dimensions. Dimensions can be in the model space and in sketches.
Limitations:
    Cannot use surfaces/faces that are not flat (must use edges to add diameters to holes)
    No hole callout tool.
    No feature recognition beyond simple selection.

## Slide 30: Using SOLIDWORKS for Model Based Definition
Feature Dimensions
Feature dimensions (including sketch dimensions used to define features) can also be employed to create annotations for product definition.

## Slide 31: Using SOLIDWORKS for Model Based Definition
Combine usage of DimXpert, Reference and Feature Dimensions
A mixture of DimXpert and Reference Dimensions is a likely solution for many environments, where each tool can be used to accomplish gaps in the other.
  Feature dimensions can also be applied to this mix, but will require more finite control of which dimensions are shown and hidden.
¡¤

## Slide 32
SOLIDWORKS MBD 2017
Brief overview

## Slide 33: SOLIDWORKS MBD
Tools
3D Views
Dynamic Annotation Display
3D PDF Template Editor
3D PDF Publisher
¤

## Slide 34: 3D Views
A method to save a particular view and settings, similar to drawing views.
Capture Saves:
  Selected Annotation Views
  Text display settings
  Display state
  Configuration
Restored with just one click.

## Slide 35: Dynamic Annotation Display
Setting to display only annotations that relevant to the current model orientation.
As the model is rotated, annotations fade out and appear as they become aligned to the current model view.

## Slide 36: 3D PDF Template Editor
Provides the ability to create and edit 3D PDF Templates for use with 3D PDF Publisher.
Many tools allow you to create objects of various functions on your 3D PDFs.

## Slide 37: 3D PDF Publisher
Allows you to create 3D PDFs of your models and annotations utilizing 3D Views, annotation views and other elements.
3D PDFs will be compatible with current Adobe Acrobat releases with the need for 3rd party software.

## Slide 38: Prismatic Example
Walk through on prismatic use case with DimXpert

## Slide 39: Organic Example
Walk through on organic part use case with DimXpert